## Slide 1: Building A Network Sample Configurations V1.2

## Slide 2
Subnet - Wild Card and Mask Table |  |  | 
Subnet Mask | Prefix | Nos Host Bits | Nos Hosts
 |  | 20 | 1
 |  | 21 | 2
255.255.255.252 | (32-2) -> /30 | 22 | 4
255.255.255.248 | (32-3) -> /29 | 3 | 8
255.255.255.240 | (32-4) -> /28 | 4 | 16
255.255.255.224 | (32-5) -> /27 | 5 | 32
255.255.255.192 | (32-6) -> /26 | 6 | 64
255.255.255.128 | (32-7) -> /25 | 7 | 128
255.255.255.0 | (32-8) -> /24 | 8 | 256
255.255.254.0 | (32-9) -> /23 | 9 | 512
255.255.252.0 | (32-10) -> /22 | 10 | 1024
255.255.248.0 | (32-11) -> /21 | 11 | 2048
255.255.240.0 | (32-12) -> /20 | 12 | 4096
255.255.224.0 | (32-13) -> /19 | 13 | 8192
255.255.192.0 | (32-14) -> /18 | 14 | 16384
Subnet Wild Card
0.0.0.3
0.0.0.7
0.0.0.15
0.0.0.31
0.0.0.63
0.0.0.127
0.0.0.255
0.0.1.255
0.0.3.255
0.0.7.255
0.0.15.255
0.0.31.255
0.0.63.255

## Slide 3: ACL Overview
ACL Case Sensitivity
ACL names are case sensitive eg aclvlanXXX and AclVlanXXX are different ACLs
Should decide to use either all uppercase - ACLVLANXXX or all lowercase – aclvlanXXX names to reduce errors
ACL Rule Order
ACL rules in the access list should be in order of most specific to least specific
The last rule should be permit All other access
ACL Placement Rules
Standard ACL – place as close as possible to destination network or device, to avoid unnecessarily blocking traffic
Extended ACL – place as close as possible to source network or device, to block traffic earlier to reduce congestion
ACL Trouble Shooting
show access-lists
clear access-list counters
Use the following for testing the rules: ping, telnet, a browser
ACL Wild Card
ACLs use Wild Cards

## Slide 4: ACL Templates
ACL for VLAN XXX on R1 Router
The Access List – Extended Named (create in Notepad, then paste into router config mode)
no ip access-list extended ACLVLANXXX (Delete previous version of the ACL for VLAN XXX )
ip access-list extended ACLVLANXXX (Self-documenting, the ACL for VLAN XXX, ! means comment)
! Only permit HTTP access to ISP Packet Tracer Server0 or ISP Loopback 0 if in Lab Router
permit tcp source subnet wildcard host ip address eq www
! Deny ALL other access to ISP Packet Tracer Server0 or ISP Loopback 0 if in Lab Router
deny ip source subnet wildcard host ip address
! Permit ping reply (echo-reply) to a destination – PCs in VLAN YYY subnet
permit icmp source subnet wildcard destination subnet wildcard echo-reply
! Deny PING request to a destination - PCs in VLAN YYY subnet
deny icmp source subnet wildcard destination subnet wildcard
! Permit access to The Internet
permit ip any any
ACL Placement - On Sub Interface G0/0/1.XXX on R1 Router
interface G0/0/1.XXX
ip access-group ACLVLANXXX in

## Slide 5: ACL Templates
ACL to control Telnet Access to R1 and R2 Routers
The Access List – Standard Named (create in Notepad, then paste into router config mode)
! On R1
no ip access-list standard ACLTELNET
ip access-list standard ACLTELNET
! Permit VLANXXX Telnet Access to R1
permit source subnet wildcard
deny any
! On R2
no ip access-list standard ACLTELNET
ip access-list standard ACLTELNET
! Deny VLANXXX Telnet Access to R2
deny source subnet wildcard
permit any
Interface Placement - line vty 0 4, on R1 and R2 Routers
line vty 0 4
password cisco
login
access-class ACLTELNET in

## Slide 6: DHCP Configuration
Configure DHCP pools on either R1 or R2
service dhcp (turns on DHCP service)
ip dhcp pool poolVLANXXX
network subnetwork subnetwork mask
default-router ip address of G0/0/1.XXX
ip dhcp pool poolVLANYYY
network subnetwork subnetwork mask
default-router ip address of G0/0/1.YYY
  Configure a ip helper address on R1 if pools on R2
Trouble Shooting Commands
  show ip dhcp pool
  show ip dhcp binding
  clear ip dhcp binding *
  debug ip dhcp server events
  open DOS CMD window on PC1 and PC2 – ipconfig /release then ipconfig /renew

## Slide 7: NAT Configuration
Configure on Router R2
  The NAT Public Address Pool, is provided by the ISP eg 135.12.64.0/25, this is a range of ip addresses, divide 3 ways, do not VLSM
  Address Pool Nat Pools
ip nat pool POOLVLANXXX starting IP address ending of IP address> netmask ?.?.?.?
ip nat pool POOLVLANYYY starting IP address ending of IP address> netmask ?.?.?.?
  ip nat pool POOLVLAN1 starting IP address ending of IP address> netmask ?.?.?.?
  NAT Access Control Lists
  ip access-list extended ACLVLANXXX
  permit ip source subnet wildcard any
  ip access-list extended ACLVLANYYY
  permit ip source subnet wildcard any
  ip access-list extended ACLVLAN1
  permit ip source subnet wildcard any
  Establish dynamic source translation by binding the pools with the access control lists
  ip nat inside source list ACLVLANXXX pool POOLVLANXXX
  ip nat inside source list ACLVLANYYY pool POOLVLANYYY
  ip nat inside source list ACLVLAN1 pool POOLVLAN1
  Specify inside and outside interfaces:
  interface s0/1/0
  interface s0/1/1
  interface loopback 0
  Overload each NAT pool
Trouble Shooting Commands
  show ip nat translations
  clear ip nat translation *
  show ip nat statistics
  debug ip nat
  debug ip nat detailed

## Slide 8: Routing Configuration Rules
Each router should only advertise its internal directly connected networks
Routing updates must not be sent to LANs/VLANs
A default route to the Internet should only be configured on the gateway router
Only the gateway router must advertise the default route to the internal routers
The ISP router
  If the company is using:
    a public network address, the ISP should have a static route pointing to the corporate’s public Network with the relevant class A, B, C mask
    a private network address, the ISP should have a static route pointing to the corporate’s public NAT Pool with relevant mask
Do not configure the ISP router with a routing protocol advertising the corporate’s network

## Slide 9: OSPF Configuration ONLY if Specified
Configure on Internal R1 Router
router OSPF 9 (9 is just a process id, routers may use different process ids)
network ?.?.?.? ?.?.?.? area 0 (VLAN XXX, ospf routers exchange updates with routers in the same area)
network ?.?.?.? ?.?.?.? area 0 (VLAN YYY, ? wildcard is inverse of subnet mask)
network ?.?.?.? ?.?.?.? area 0 (VLAN 1 wildcard is inverse of subnet mask)
network ?.?.?.? ?.?.?.? area 0 (Serial Link – R1 to R2)
passive-interface interface (As appropriate to avoid unnecessarily sending routing information)
Configure on Internal Gateway R2 Router
router OSPF 10
network ?.?.?.? ?.?.?.? area 0 (Loopback Database LAN)
network ?.?.?.? ?.?.?.? area 0 (Serial Link – R1 to R2)
ip route ?.?.?.? ?.?.?.? S0/1/1 (The default route to the Internet)
default-information originate (Advertise default route to other internal routers)
passive-interface interface (As appropriate to avoid unnecessarily sending routing information)
Configure on External ISP R3 Router (OSPF is not configured in ISP)
ip route ?.?.?.? ?.?.?.? S0/1/1 (ISP configure a static route to Public NAT Pool)

## Slide 10: EIGRP Configuration ONLY if Specified
Configure on Internal R1 Router
router EIGRP 15 (15 is the autonomous system number, both routers need to use the same number in order to exchange updates)
network ?.?.?.?> ?.?.?.? (wildcard is inverse of subnet mask, ? means insert)
“
passive-interface interface (As appropriate to avoid unnecessarily sending routing information)
Configure on Gateway R2 Router
router EIGRP 15
network ?.?.?.? ?.?.?.? (wildcard is inverse of subnet mask, ? means insert)
“
ip route 0.0.0.0 0.0.0.0 S0/1/1 (The default route to the Internet)
redistribute static (Advertise default route to other internal routers)
passive-interface interface (As appropriate to avoid unnecessarily sending routing information)
Configure on ISP R3 Router (EIGRP is not configured in ISP)
ip route ?.?.?.? ?.?.?.? S0/1/1 (ISP configure a static route to Public NAT Pool)

## Slide 11: Inter-VLAN Routing Configuration
Configure on the required Router
interface G0/0/1
description The Physical Interface
no shutdown
interface G0/0/1.1
description A logical Sub Interface
description VLAN 1 VLAN Management
encapsulation dot1q 1
ip address address subnet mask
interface G0/0/1.vlan id
description A logical Sub Interface
description VLAN vlan Id vlan name
encapsulation dot1q vlan id
ip address address subnet mask
etc ……

## Slide 12: Switch Configuration
Configure VLANs
vlan XXX
name Dogs
vlan YYY
name Cats
Configure IP address for management vlan
interface VLAN 1
ip address address mask (This allows the switch to be configured remotely via Telnet)
Configure Default Gateway
ip default-gateway ip address of router interface (Use VLAN 1 subinterface IP address)

## Slide 13: Switch Configuration
Configure a switch ACCESS port (note you can specify a range of switch ports):
interface fa 0/3 (or interface range fa 0/3 – 5)
switchport access vlan <number> (assigns port to a vlan)
switchport mode access (sets port to access, for PCs)
switchport port-security (enables port security, do not forget this command)
switchport port-security maximum 1 (maximum of 1 mac address(es) can stick)
switchport port-security mac-address sticky
switchport port-security violation shutdown (shuts down port, default when security turned on)
OR
switchport port-security violation protect (protects, but does not shut down the port)
Configure a static MAC address entry in Mac Address Table
mac address-table static AAAA.BBBB.CCCC vlan YYY interface fa 0/24
(replace AAAA.BBBB.CCCC with the mac address of the PC)

## Slide 14: Switch Configuration
Configure a switch TRUNK port
2960 Series Switch
interface G0/1
switchport mode trunk (sets port to trunk)
3650 Series Switch
interface G0/1
switchport mode trunk (sets port to trunk)
3560 Series Switch
interface Fa0/1
switchport trunk encapsulation dot1q (must specify 802.1q encapsulation)
switchport mode trunk (sets port to trunk)

## Slide 15: Switch Commands
Managing the MAC Address Table
show mac address-table (displays entries in table)
show mac address-table dynamic (displays only dynamic entries in table)
clear mac address-table (deletes all entries from table)
clear mac address-table dynamic (deletes only dynamic entries from table)
Re-activating a switch port that has been violated
When a violation causes a switch port to block traffic, it must be re-activated
This is achieved by doing a shutdown then a no shutdown on the switch port, refer below:
interface fa0/10
shutdown
(wait until shutdown confirmed)
no shutdown

## Slide 16: PPP Configuration
Configure on Router R2 Gateway
interface S0/1/1
description Link to R3
ip address address subnet mask
encapsulation ppp
no shutdown
Configure on Router R3 ISP
interface S0/1/1
description Link to R2
ip address address subnet mask
encapsulation ppp
no shutdown
PPP Trouble Shooting Commands
  debug ppp negotiation
  debug ppp packet

## Slide 17: CHAP Configuration – Create User Accounts
Configure on Router R2 Gateway
username R3 password cisco (username and password are case sensitive)
interface S0/1/1
ppp authentication chap
Configure on Router R3 ISP
username R2 password cisco
interface S0/1/1
ppp authentication chap
The Password Problem
  You need to ensure the password does not have spaces at the front or the end else the authentication will fail
PPP Trouble Shooting Commands
  debug ppp authentication

## Slide 18: Other Management Commands
How to save a Router/Switch configuration: copy run start
How to remove a Router/ Switch configuration: write erase, then reload (say no when asked if want to save the changes)
How to remove the VLAN configuration on a Switch: delete vlan.dat
Some show commands
  show ip interface brief: very important to know how to read the output
  show run: displays the running configuration file (check running settings)
  show start: displays the startup config file (check the settings that will take effect after a reboot)
  show version: IOS version, image file name, last rebooted, config-reg value, etc

## Slide 19: How to configure SSH – Secure Shell
1. Configure switch or router with a hostname:
hostname S1
2. Configure a local user account:
username labuser privilege 15 secret cisco (always use cisco as password)
3. Configure domain name:
ip domain-name scenario.lab
4. Configure SSH Certificate:
crypto key generate rsa general-keys modulus 1024
5. Configure Line vty
line vty 0 15 (4 for a router)
transport input SSH
login local
end

## Slide 20: How to configure SSH – Secure Shell
Test SSH
  ssh –l labuser <ip address> (l is a letter)
2. SSH Connection Options
  config t
    ip ssh time-out 60
    ip ssh authentication-retries 4
  exit

## Slide 21: PC Command Window Useful Trouble Shooting Commands
ipconfig
  Allows you check your PC’s addresses
  ipconfig /all
  ipconfig /? for help
  To request the DHCP server to release or renew the PC’s IP address use:
    ipconfig /release, ipconfig /renew
netstat
  Displays the TCP/IP network protocol statistics and information
  netstat –a
  netstat –e
  netstat –s
  netstat /? for help
nbtstat
  Displays protocol statistics and current TCP/IP connections
  nbtstat –n
  nbtstat /? for help

## Slide 22: PC Command Window Useful Trouble Shooting Commands
arp
  Displays the Address Resolution table
  arp -a
  arp /? for help
route print
  Displays the routing table of your PC
  route /? for help
ping
  ping 127.0.0.1 Checks your PC’s IPv4 Protocol stack
  ping 192.168.1.10 ping a destination
  ping /? for help
tracert
  Traces individual hops to the destination
  tracert 192.168.1.10
  tracert /? for help