## Slide 1: A Systematic Approach to Building A Network Task By Task V1.1
To build a Network, we must use a Systematic Approach to build the network:
  Determine Task Order
  For each Task: configure, test, troubleshoot

## Slide 2
(Internal)
Router
R1
Switch S3
3650
Company Network Address
G0/0/1
S0/1/0
S0/1/0
Routing Protocols
RIP/EIGRP/OSPF
(Gateway)
Router
R2
G1/0/11
(ISP)
Router
R3
Trunk for Inter-VLAN
Routing
ISP Link
Network Address
PC1
VLANXXX
PC2
VLANYYY
G1/0/13
G1/0/24
Loopback 0
Server LAN
Database Server
S0/1/1
S0/1/1
PC VAN VM
If in lab
PC Ethernet VM
If in lab
Task 1 - Prepare Network Topology Diagram
Internal
External
NAT Public
Address POOLS
“The Internet”
Internet Address 1
Packet Tracer
External
Server-PT
Server0
Ethernet Interface
OR
Loopback 0
if in Lab Router
Internet Address 2
Packet Tracer
External
Server-PT
Server1
Ethernet Interface
OR
Loopback 1
if in Lab Router
Loopback 2
Internet Address 3
Loopback 3
Internet Address 4

## Slide 3
1. Prepare Network Topology Diagram
2. Prepare the VLSM Design
a) It is important to get your addressing scheme correct and documented.
b) Use a VLSM calculator
3. In Lab Kits
a) Book a Kit for 4 hours
b) Select devices needed, check each device is clean, if not, clean it
4. Ethernet Cable Connections, refer Network Topology Diagram
a) PC to patch panel
b) Patch panel to switch
c) Switch to Router
5. Device Host Names
a) All devices must be configured with a host name - eg hostname R1
6. Helpful Configurations
a) Configure the line console on each router and switch, as shown below:
line console 0
logging synchronous (stops system messages overwriting your typing)
exec-timeout 0 0 (ensures you do not return to user executive mode)
b) Turn off DNS (Domain Name Service)
no ip domain-lookup (ensures if you miss-type a command, the router will not try to resolve the
command as a URL web address)
Building A Network - Task Order

## Slide 4: Building A Network - Task Order
7. Message of the Day (MOTD) Banner Configuration
You must configure a MOTD Banner, recording your student id, family name and session time, on all routers and switches, as shown below:
banner motd &
Welcome to Hostname
Your Student Id, Your Family Name, Your Session Time
&
8. Switch Configuration
a) Create VLANs
b) Configure trunk ports
c) Configure access ports and allocate to correct vlan
d) Switch Management - Configure ip address and default gateway for each switch
e) Configure Port Security if required
9. Trouble Shooting VLANs
a) To check VLANs created, use – show vlan brief
b) Remove unwanted Vlans, eg – no VLAN 20
10. Trouble Shooting Port Security (if configured)
a) To check port security is enabled, use - show port-security
b) A table will be displayed showing the security status of the switch ports

## Slide 5: Building A Network -Task Order
11. Network IP Address Configuration
a) Configure ALL the router serial and loopback interfaces with ip addresses and descriptions
b) Configure Inter-VLAN Routing
  Create separate sub-interfaces
  Assign each sub-interface with an ip address and description
c) PC Configuration
- Configure each PC with IP address and default gateway
d) Switch Management
- Check each switch is configured with an ip address and a default gateway for the Management VLAN
12. Trouble Shooting Trunking – between Switch and Router
a) To check Trunking is activated, on switch(es) use – show interface trunk
b) Check correct interface has been configured for trunking all vlans

## Slide 6: Building A Network - Task Order
13. Trouble Shooting Point-to-Point Single Link Testing
a) This test is to check that each individual link in the network is working - interfaces on and have correct ip addresses
b) Ping – ensure you can ping from one end of each link to the other:
  PC to Router in same subnet/VLAN/network.
  PC to PC in same subnet/VLAN/network
  Switch to Router
  Router to each direct neighbour Router over a serial link.
c) Link NOT working ? - Common problems:
  Physical connection not made.
  An incorrect IP address or subnet mask is configured on one interface of a link
  The interface is shutdown.
14. Trouble Shooting Inter-VLAN Routing Testing
a) This test is to check Inter-VLAN routing is working
b) Ping PC1 – VLAN XXX to PC2 – VLAN YYY
c) Ping PC1 – Switch S3 etc
d) On Routers – show arp, to check the IP address to MAC address mapping
15. Trouble Shooting Telnet to Switch (if required)
a) To check you can telnet to the switch
b) From PC1 DOS command window – telnet to the switch
c) Common problems:
  Switch Vlan1 interface shutdown
  Switch has no default gateway IP address
  Switch Line vty not configured with login and password
  Inter-VLAN routing failure

## Slide 7: Building A Network - Task Order
16. Routing Protocol Configuration
a) Internal Routers
  RIP advertise whole network
  OSPF/EIGRP using wildcards for each subnet
  Configure passive-interface as appropriate to avoid sending unnecessary routing information to subnets
b) Gateway Router
  RIP advertise whole network
  OSPF/EIGRP using wildcards for each subnet
  Do not advertise the ISP Link Network Address
  Configure passive-interface as appropriate to avoid sending unnecessary routing information
  Configure default route to ISP Router
  Advertise default route to Internal Routers
c) ISP Router
  Do not configure OSPF/EIGRP/RIP
  Configure loopbacks for Web Servers (If you are using Packet Tracer may need to use Server Devices)
  Configure static route, use the Company’s Network Address, to the Gateway Router
17. Trouble Shooting OSPF/EIGRP Neighbor Adjacency (if required)
a) Verify that the routers have formed an adjacency with each other, use - show ip ospf/eigrp neighbor
b) Adjacency NOT Formed ? - If an adjacency has not formed it could be due to:
i) subnet masks on each end of link do not match
ii) the directly connected subnet is not included in the network statements
c) Other trouble shooting commands: show ip protocols
18. Trouble Shooting Routing - Presence of Subnets
a) Internal Routers
- Use show ip route to display the routing table on each router:
- Check all the subnets are present
- Check there is a gateway of last of resort
b) Common problems:
  Routing protocol is not advertising a subnet
  An interface is down
  Static or Default route not configured on Gateway Router

## Slide 8: Building A Network - Task Order
19. Trouble Shooting Internal Private End-to-End Path Testing
a) This test is to check that the internal routing - static and dynamic, is working.
b) Use debug ip icmp on Gateway router R2 to check ping request arrives
c) Ping from PC Hosts in VLAN XXX and VLAN YYY to Database Server loopback on Gateway Router
d) Use traceroute to pin point problems.
e) Internal Private End-to-End Path Test Failed ? - Common problems:
  Default gateway IP address not configured on a PC.
  PC connected to incorrect interface.
  Subnet not advertised
  Subnet missing from routing table
  Default route not advertise
20. NAT Configuration (if required)
    a) Configure NAT Pools on the Gateway Router R2
    - Create separate NAT Pools and ACLs for VLANs 1, XXX, YYY
    - Overload each NAT pool
    b) ISP Router R3
    - Configure a static route to the public NAT Pool address on Gateway Router R2
21. Trouble Shooting NAT - Internal Private to External Public End-to-End Path Testing (if required)
a) This test is to check that NAT is working - that the private IP address is being translated to a public IP address
b) Use debug ip nat on Gateway Router to view the NAT translations
c) Use debug ip icmp on ISP router to check ping request arrives
d) Ping from PC Hosts in VLAN XXX and VLAN YYY to the Internet – pick an External Web Server
e) NAT Failed ? – Common Problems:
  ACL and Pool names are case sensitive, check names are correct
  ACL incorrectly configured
  NAT pool incorrectly configured
  Binding of ACL to NAT Pool incorrectly configured
  Inside and outside interfaces incorrectly or not configured
  On ISP static route is not pointing to NAT pool
f) Useful commands, use - show ip nat translations, debug ip nat

## Slide 9: Building A Network - Task Order
22. DHCP Configuration (if required) Options: a) or b)
    a) DHCP on Internal R1
    - Create separate DHCP Pools for VLANs XXX and YYY
    - Exclude the first four IP addresses
    - Configure PC1 and PC2 to obtain an IP address automatically
    b) DHCP on Gateway Router R2
    - Configure helper ip address for DHCP on Internal Router
    - Create separate DHCP Pools for VLANs XXX and YYY
    - Exclude the first four IP addresses
    - Configure PC1 and PC2 to obtain an IP address automatically
23. Trouble Shooting DHCP (if required)
a) Use debug ip dhcp server events on R1 or R2 Router, to view the DHCP process
b) Open DOS CMD window on PC1 and PC2 – ipconfig /release then ipconfig /renew
c) Addresses obtained ? NO – check router configuration,
use – show ip dhcp pool, show ip dhcp binding, show run
24. HTTP Servers
a) On In Lab Routers
  Configure a HTTP server on ISP Router, use – ip http server
b) Packet tracer
  If you are using Packet Tracer you must configure Web Servers and connect the servers to the ISP Router
c) Allows you to test your ACLs using a Browser
25. Telnet Access to Routers (if required)
a) Configure line vty with password cisco and login, so you can connect to each router can via Telnet
b) NO enable password is required as you are NOT configuring the router
c) This allows you to test your ACLs using Telnet.

## Slide 10: Building A Network - Task Order
26. Point-to-Point Protocol (PPP) Configuration (if required)
a) Configure the link between Gateway Router R2 and ISP Router R3 as PPP link
b) Ping across the link between Gateway Router R2 and ISP Router R3 to check it is working
27. CHAP Configuration (if required)
a) Configure CHAP authentication on the link between Gateway Router R2 and ISP Router R3
28. Trouble Shooting CHAP (if required)
a) Ping across the link between Gateway Router R2 and ISP Router R3 to check it is working
b) Ping failed ? – Common problems:
  Host name incorrectly configured
  Password incorrectly configured with space at front
  Encapsulation incorrectly configured
c) To check authentication, use - debug ppp authentication

## Slide 11: Building A Network - Task Order
29. Access List Requirements
a) Create a NAMED Extended ACL for VLAN XXX based on following requirements:
  PCs in VLAN XXX permitted HTTP access to ISP Packet Tracer Server0 or ISP Loopback 0 if in Lab Router and denied ALL other access to this Server.
  PCs in VLAN XXX denied PING request to PCs in VLAN YYY
  PCs in VLAN XXX permitted PING reply to PCs in VLAN YYY
  PCs in VLAN XXX permitted ALL access to the Internet – all the external Servers
c) Create a NAMED Extended ACL for VLAN YYY based on following requirements:
  PCs in VLAN YYY denied ALL access to Database Server LAN
  PCs in VLAN YYY permitted ALL access to the Internet – all the external Servers
  ALL means IP
d) Create NAMED Standard ACLs to control Telnet access to the routers based on following requirements:
  ONLY PCs in VLAN XXX permitted TELNET access to Internal Router R1
  ONLY PCs in VLAN XXX denied TELNET access to Gateway Router R2
e) You need to be systematic in our approach to translating the above requirements into a set of rules – the ACL
statements, which then must be tested to ensure the above requirements have been satisfied.

## Slide 12: Building A Network - Task Order
30. Creating and Configuring NAMED Access Lists
a) Use Notepad to create your ACLs, note ACL names are case sensitive eg aclvanXXX and AclvlanXXX are different acls
b) Identify each requirement then configure an ACL rule for each requirement.
c) Create a NAMED access list in Notepad, consider the ordering of the rules, use the following template:
! ACL for VLAN <No> on Router <router name>
! Deletes previous version of access list
no ip access-list extended ACLVLAN<No>
! Insert Latest version of access list
ip access-list extended ACLVLAN<No>
<Your ACL rules follow>
! For most situations this should be the last rule ie permit all other access to “The Internet”
permit ip any any
d) Combine ACL rules as required to form your access list, carefully consider the order in which the rules should be arranged.
e) Paste ACL from Notepad into router (router must be in global configuration mode)
f) Configure ACL on correct interface
31. Trouble Shooting Access Lists
It is important to verify that the ACL rules actually work as intended, refer to the steps below:
  1. Use show access-lists
    If all rules tested go to 5
    Else Identify which rule you want to test
  2. Use clear access-list counters
    Clear any counts against the rules
  3. Go to PC in VLAN<Id> perform test eg Ping, Telnet, Browser etc to trigger a match with the identified rule
  4. Use show access-lists
  Was the identified rule matched ?
    Yes – rule action correct, Repeat process, go to 1
    No – Debug
      Was another rule matched ?
      Where no rules matched ?
      Check syntax and order of rules – make changes – Repeat process go to 1
5. Trouble Shooting completed