## Slide 1
Network Topology Exercise A V1.0
From
Routing Tables
to
Network Topology

## Slide 2: Network Topology Exercise A
You need to understand the contents of the routing table to determine:
  the Topology of the network
  if there is a Problem with the operation of the routing protocol

## Slide 3: Routing Table Entries – show ip route
The contents of the routing table:
Link local route interfaces - Added to the routing table when an interface is configured. Shows IP address of the Interface.
Connected interfaces – directly connected networks Added to the routing table when an interface is configured and active.
Static routes - Added when a route is manually configured and the exit interface is active.
Dynamic routing protocol – remote networks Added when RIP, EIGRP or OSPF are implemented and networks are identified.
Notes: 1.3.1.2 Routing Table Sources

## Slide 4: Tasks
Given Routing Tables for R1, R2 and R3
Draw a Network Topology Diagram
  Show all interfaces with their ip addresses
  Show all LAN subnets with their subnet addresses
  Show all Serial subnets with their subnet addresses
Answer Questions on the information contained in the routing tables
Notes: 2.2.1.6 Verify a Static Route

## Slide 5: R1 Router - Routing Table
R1# show ip route
10.0.0.0/8 is variably subnetted, 3 subnets, 2 masks
C 10.1.1.0/30 is directly connected, Serial0/0/0
L 10.1.1.1/32 is directly connected, Serial0/0/0
R 10.2.2.0/30 [120/1] via 10.1.1.2, 00:00:21, Serial0/0/0
172.30.0.0/16 is variably subnetted, 2 subnets, 2 masks
C 172.30.10.0/24 is directly connected, FastEthernet0/1
L 172.30.10.1/32 is directly connected, FastEthernet0/1

## Slide 6: R2 Router - Routing Table
R2# show ip route
10.0.0.0/8 is variably subnetted, 4 subnets, 2 masks
C 10.1.1.0/30 is directly connected, Serial0/0/0
L 10.1.1.2/32 is directly connected, Serial0/0/0
C 10.2.2.0/30 is directly connected, Serial0/0/1
L 10.2.2.2/32 is directly connected, Serial0/0/1
R 172.30.0.0/16 [120/1] via 10.2.2.1, 00:00:23, Serial0/0/1
[120/1] via 10.1.1.1, 00:00:09, Serial0/0/0
209.165.201.0/24 is variably subnetted, 2 subnets, 2 masks
C 209.165.201.0/24 is directly connected, FastEthernet0/0
L 209.165.201.1/32 is directly connected, FastEthernet0/0

## Slide 7: R3 Router - Routing Table
R3# show ip route
10.0.0.0/8 is variably subnetted, 3 subnets, 2 masks
C 10.2.2.0/30 is directly connected, Serial0/0/1
L 10.2.2.1/32 is directly connected, Serial0/0/1
R 10.1.1.0/30 [120/1] via 10.2.2.2, 00:00:23, Serial0/0/1
172.30.0.0/16 is variably subnetted, 2 subnets, 2 masks
C 172.30.30.0/24 is directly connected, FastEthernet0/1
L 172.30.30.1/32 is directly connected, FastEthernet0/1

## Slide 8: Questions
What does variably subnetted mean ?
Given, from R2 routing table:
R 172.30.0.0/16 [120/1] via 10.2.2.1, 00:00:23, Serial0/0/1
[120/1] via 10.1.1.1, 00:00:09, Serial0/0/0
  What does [120/1] tell Us ?
  What does 00:00:23 tell Us ?
  Why are RIP updates from 172.30.0.0/16 coming from two different interfaces ?
R1 cannot see 172.30.30.0/24 subnet, Why ?
  R1 and R3 cannot see network 209.165.201.0/24, Why ?
Notes: 2.2.1.6 Verify a Static Route