## Slide 1: Network Topology Exercise B V1.0
Overview
You have been given the routing tables of three routers: London, Paris, and Rome
Given the information provided in each of the router’s routing table you will be required to complete the following tasks:
  Create a Network Topology Diagram, refer page 2
  Answer questions, refer page 8, regarding the Topology Diagram and Routing Tables

## Slide 2: Task 1 - Create a Network Topology Diagram
Refer to the Network Topology Diagram Layout, on page 3, which your diagram must conform with.
Refer to the Routing Tables, on pages 4 to 6, which contain the information needed to create your diagram.
Your can plan you diagram by creating a draft copy on page 7.
For assessment, your final diagram must be on page 8
On your final diagram show the following:
  all interfaces, serial, fastethernet and loopback on each router
  all serial point-to-point links between routers and links to LANs/VLANs
  all network addresses with prefix

## Slide 3
Rx
Rx
Task 1 - Network Topology Diagram Layout
Your answer must conform with the Drawing Symbols and Layout Below
Serial Link
LAN Link
S0/0/0
S0/0/1
Fa0/0
Fa0/1
Network Address/Prefix
Network Address/Prefix
Rx
VLAN Link
VLAN ID/Network Address/Prefix
VLAN ID/Network Address/Prefix
VLAN ID/Network Address/Prefix
Serial Link
Network Address/Prefix
S0/0/1)
S0/0/0)
Loopback0
(ip address/prefix)

## Slide 4
Paris (R1) Routing Table
Codes: C - connected, S - static, R - RIP, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
* - candidate default
Gateway of last resort is 55.0.8.42 to network 0.0.0.0
55.0.0.0/8 is variably subnetted, 5 subnets, 5 masks
C 55.0.8.40/30 is directly connected, Serial0/0/0
C 55.0.8.32/29 is directly connected, FastEthernet0/1.1
C 55.0.7.0/27 is directly connected, Loopback0
C 55.0.4.0/23 is directly connected, FastEthernet0/1.25
C 55.0.0.0/22 is directly connected, FastEthernet0/1.15
O*E2 0.0.0.0/0 [110/1] via 55.0.8.42, 00:24:35, Serial0/0/0
Routing Tables

## Slide 5
Routing Tables
London (R2) Routing Table
Codes: C - connected, S - static, R - RIP, M - mobile, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
* - candidate default
Gateway of last resort is 0.0.0.0 to network 0.0.0.0
201.5.5.0/30 is subnetted, 1 subnets
C 201.5.5.0 is directly connected, Serial0/0/1
55.0.0.0/8 is variably subnetted, 6 subnets, 6 masks
C 55.0.8.40/30 is directly connected, Serial0/0/0
O 55.0.8.32/29 [110/65] via 55.0.8.41, 00:25:58, Serial0/0/0
O 55.0.7.1/32 [110/65] via 55.0.8.41, 00:32:24, Serial0/0/0
O 55.0.4.0/23 [110/65] via 55.0.8.41, 00:25:58, Serial0/0/0
O 55.0.0.0/22 [110/65] via 55.0.8.41, 00:25:58, Serial0/0/0
C 55.0.8.0/27 is directly connected, Loopback0
S* 0.0.0.0/0 is directly connected, Serial0/0/1

## Slide 6
Rome (R3) Routing Table
Codes: C - connected, S - static, R - RIP, M - mobile, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
* - candidate default
Gateway of last resort is not set
201.5.5.0/30 is subnetted, 1 subnets
C 201.5.5.0 is directly connected, Serial0/0/1
S 55.0.0.0/8 [1/0] via 201.5.5.2
160.1.0.0/32 is subnetted, 1 subnets
C 160.1.1.1 is directly connected, Loopback0
Routing Tables

## Slide 7
Task 1 - Network Topology Diagram

## Slide 8: Task 2 – Questions regarding the Topology Diagram and Routing Tables
  List the routers that use OSPF
  List the routers that use static routes
  List the routers that use only static routes
  For each router determine how many static routes are mapped to exit interfaces
  For each router determine how many static routes are mapped to next hop IP addresses
  Which router is the gateway to Internet
  List the routers that learn their gateway via OSPF
  List the routers that use a static route to point to the gateway
  For each Router list the networks learnt via OSPF
  On London what does[110/65] mean
  On London what does 00:25:58 mean
  Which router is the ISP
  List the routers that have LANs, and how many LANs are there
  What are the IP addresses of the interfaces on the London router